## Slide 1
EIGHT CASES / ONE LEARNING METHOD / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
LAB 03
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
01
Running
Running: Aerial Gait with Intended Progress
Environment design · PPO · Honest verification
BUILD → TRAIN → VERIFY → EXPLAIN
Notes: Running: Aerial Gait with Intended Progress Use case: Teach why fast motion is not enough: a running policy must survive, follow the commanded direction, alternate support, and show true both-feet aerial phases. Start by explaining the difference between a simulation training pipeline and skill mastery. The cover image is a frame decoded from this case's actual rollout, not generated artwork. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 2
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
What you will build — and what the evidence says
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
02
01
Use case: Teach why fast motion is not enough: a running policy must survive, follow the commanded direction, alternate support, and show true both-feet aerial phases.
02
By the end: describe the scene, map observations to actions, explain the reward, trace one PPO update, run a bounded experiment, and defend an evaluation claim.
03
The policy specializes to one nominal 0.75 m/s forward command; arbitrary speed, turning, and disturbance recovery are untested.
04
Scope: local MuJoCo simulation. Do not deploy these classroom artifacts to a physical robot; hardware transfer requires a separate validated process.
Notes: What you will build — and what the evidence says Use case: Teach why fast motion is not enough: a running policy must survive, follow the commanded direction, alternate support, and show true both-feet aerial phases. By the end: describe the scene, map observations to actions, explain the reward, trace one PPO update, run a bounded experiment, and defend an evaluation claim. The policy specializes to one nominal 0.75 m/s forward command; arbitrary speed, turning, and disturbance recovery are untested. Scope: local MuJoCo simulation. Do not deploy these classroom artifacts to a physical robot; hardware transfer requires a separate validated process. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 3
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Materials and prerequisites · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
03
01
Apple Silicon Mac with installed RLX/MLX, MuJoCo, ONNX Runtime, rendering dependencies, and Node.
02
Tracked base and refinement recipes: running-base.json and running.json.
03
Studio trainer/exporter, scenario HTTP driver, independent audit_scenarios.py, and video verifier.
04
Saved base checkpoint plus adjacent normalization sidecar; both are required for the refinement stage.
Notes: Materials and prerequisites · 1/2 Apple Silicon Mac with installed RLX/MLX, MuJoCo, ONNX Runtime, rendering dependencies, and Node. Tracked base and refinement recipes: running-base.json and running.json. Studio trainer/exporter, scenario HTTP driver, independent audit_scenarios.py, and video verifier. Saved base checkpoint plus adjacent normalization sidecar; both are required for the refinement stage. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 4
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Materials and prerequisites · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
04
05
Final checkpoint, ONNX actor, evaluation JSON, physical NPZ traces, optimizer JSONL, MP4, contact sheet, and render receipt.
Notes: Materials and prerequisites · 2/2 Final checkpoint, ONNX actor, evaluation JSON, physical NPZ traces, optimizer JSONL, MP4, contact sheet, and render receipt. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 5
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Environment and policy contract · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
05
01
Nominal XML-actuator MuJoCo at 50 Hz; fixed command is 0.75 m/s forward, zero lateral speed, and zero yaw rate.
02
Observation is float32 batch x 61 with gyro, projected gravity, 14 joint offsets, lagged velocities, prior raw action, and 13 command values.
03
Absolute world position and yaw are absent; gyro yaw rate and commanded yaw rate are observable, so yaw-rate tracking is learnable.
04
Action is float32 batch x 14 raw target offsets; the environment stores raw values, clips applied offsets to [-4,4], and adds DEFAULT_POSE.
Notes: Environment and policy contract · 1/2 Nominal XML-actuator MuJoCo at 50 Hz; fixed command is 0.75 m/s forward, zero lateral speed, and zero yaw rate. Observation is float32 batch x 61 with gyro, projected gravity, 14 joint offsets, lagged velocities, prior raw action, and 13 command values. Absolute world position and yaw are absent; gyro yaw rate and commanded yaw rate are observable, so yaw-rate tracking is learnable. Action is float32 batch x 14 raw target offsets; the environment stores raw values, clips applied offsets to [-4,4], and adds DEFAULT_POSE. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 6
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Environment and policy contract · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
06
05
Episode horizon is 600 control steps or 12 seconds; domain randomization, observation noise, action delay, and random yaw are disabled.
06
The native speed curriculum is bypassed by pinning every twist command to [0.75,0,0]; head/body keep-alive commands still vary.
Notes: Environment and policy contract · 2/2 Episode horizon is 600 control steps or 12 seconds; domain randomization, observation noise, action delay, and random yaw are disabled. The native speed curriculum is bypassed by pinning every twist command to [0.75,0,0]; head/body keep-alive commands still vary. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 7
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
How this case is built: one evidence loop
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
07
01 / SCENE
Flat ground + free robot
02 / COMMAND
Requested forward velocity
03 / OBJECTIVE
Speed + aerial gait
04 / TRAIN
Base PPO → refinement
05 / VERIFY
Progress + flight phases
06 / EVIDENCE
Seed sweep + gait video
Failure is data: change one cause, retrain, and repeat the same evaluation gates.
Notes: Case-specific build flow 01 / SCENE: Flat ground + free robot 02 / COMMAND: Requested forward velocity 03 / OBJECTIVE: Speed + aerial gait 04 / TRAIN: Base PPO → refinement 05 / VERIFY: Progress + flight phases 06 / EVIDENCE: Seed sweep + gait video This is an explanatory workflow diagram, not a measured learning curve. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 8
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Build the case step by step · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
08
01
Train Running v3 from random actor and critic weights for 6,000,640 transitions using the base reward and fixed 0.75 m/s command.
02
Retain the v3 failed intended-progress verdict; it acquired an aerial gait but curved enough to fail signed command-directed displacement.
03
Copy both the v3 checkpoint and its .safetensors.json normalizer sidecar into a fresh v4 run directory.
04
Resume for 2,097,152 transitions with lower combined angular weight and new observable yaw-rate-only shaping.
Notes: Build the case step by step · 1/2 Train Running v3 from random actor and critic weights for 6,000,640 transitions using the base reward and fixed 0.75 m/s command. Retain the v3 failed intended-progress verdict; it acquired an aerial gait but curved enough to fail signed command-directed displacement. Copy both the v3 checkpoint and its .safetensors.json normalizer sidecar into a fresh v4 run directory. Resume for 2,097,152 transitions with lower combined angular weight and new observable yaw-rate-only shaping. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 9
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Build the case step by step · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
09
05
Export the deterministic actor with normalization baked in; do not substitute a raw checkpoint or mismatched sidecar.
06
Evaluate 12-second episodes with heading-anchored signed displacement, support events, foot air/contact fractions, and aerial fraction.
07
Audit seeds 501-505 against zero, random, and initial controls, then validate ONNX parity, complete MP4 decoding, and browser playback.
Notes: Build the case step by step · 2/2 Export the deterministic actor with normalization baked in; do not substitute a raw checkpoint or mismatched sidecar. Evaluate 12-second episodes with heading-anchored signed displacement, support events, foot air/contact fractions, and aerial fraction. Audit seeds 501-505 against zero, random, and initial controls, then validate ONNX parity, complete MP4 decoding, and browser playback. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 10
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
PPO: improve the actor without trusting a huge step
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
10
ratio = πnew(a | o) / πold(a | o)
Maximize mean[min(ratio × A, clip(ratio, 1 − ε, 1 + ε) × A)]
Actor: chooses joint actions. Critic: estimates future discounted reward.
A = advantage. ε = clipping range. Old log probabilities stay fixed for each collected batch.
Notes: PPO clipped surrogate This is a teaching formula, not a saved experiment value. The optimizer minimizes the negative policy surrogate plus the implementation-specific value and entropy terms. PPO clipping is not a hard KL bound; monitor KL and clip fraction. A negative policy loss or Gaussian entropy is not automatically an error. Each scenario has its own reward units and optimizer conventions. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 11
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Follow one rollout through the learner
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
11
01
Collect observations, sampled actions, old log probabilities, values, rewards and episode-boundary flags using the current stochastic actor.
02
Compute TD residuals and generalized advantage estimates (GAE). A true terminal has zero continuation value; a timeout may bootstrap the saved final observation.
03
Cut advantage traces at reset boundaries. Never bootstrap a timeout from the first observation of the next episode.
04
Reuse this batch for PPO minibatch updates, then collect fresh on-policy data. Export the deterministic actor and its observation transform for evaluation.
Notes: Follow one rollout through the learner Collect observations, sampled actions, old log probabilities, values, rewards and episode-boundary flags using the current stochastic actor. Compute TD residuals and generalized advantage estimates (GAE). A true terminal has zero continuation value; a timeout may bootstrap the saved final observation. Cut advantage traces at reset boundaries. Never bootstrap a timeout from the first observation of the next episode. Reuse this batch for PPO minibatch updates, then collect fresh on-policy data. Export the deterministic actor and its observation transform for evaluation. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 12
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Paper exercise: count samples and clip the objective
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
12
01
Illustrative arithmetic, NOT this run: 16 environments × 128 steps = 2,048 fresh transitions per rollout. Four epochs reuse those transitions; they do not create 8,192 new samples.
02
With ε = 0.2, ratio = 1.4 and A = +2: min(2.8, 2.4) = 2.4. The minimized policy term is −2.4 before averaging and additional loss terms.
03
With the same ratio and A = −2: min(−2.8, −2.4) = −2.8. Explain why clipping is asymmetric once the sign of the advantage changes.
04
Run from repo root: python3 docs/microduck-training-student-book/learning_lab.py --gae. This is a deterministic arithmetic lab, not new policy training.
Notes: Paper exercise: count samples and clip the objective Illustrative arithmetic, NOT this run: 16 environments × 128 steps = 2,048 fresh transitions per rollout. Four epochs reuse those transitions; they do not create 8,192 new samples. With ε = 0.2, ratio = 1.4 and A = +2: min(2.8, 2.4) = 2.4. The minimized policy term is −2.4 before averaging and additional loss terms. With the same ratio and A = −2: min(−2.8, −2.4) = −2.8. Explain why clipping is asymmetric once the sign of the advantage changes. Run from repo root: python3 docs/microduck-training-student-book/learning_lab.py --gae. This is a deterministic arithmetic lab, not new policy training. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 13
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Reward design: what the agent is paid to do · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
13
01
keep_pace 12: baseline-subtracted Gaussian command tracking, so standing at a nonzero command scores zero.
02
track_turn 2: combined yaw, roll, and pitch rate tracking; reduced from 8 in the base recipe.
03
yaw_tracking 8: focused Gaussian on observable gyro yaw rate versus commanded yaw rate.
04
flight 4: rewards both feet airborne only while upright and moving in the commanded direction; air_time 1 rewards per-foot flight windows.
Notes: Reward design: what the agent is paid to do · 1/2 keep_pace 12: baseline-subtracted Gaussian command tracking, so standing at a nonzero command scores zero. track_turn 2: combined yaw, roll, and pitch rate tracking; reduced from 8 in the base recipe. yaw_tracking 8: focused Gaussian on observable gyro yaw rate versus commanded yaw rate. flight 4: rewards both feet airborne only while upright and moving in the commanded direction; air_time 1 rewards per-foot flight windows. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 14
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Reward design: what the agent is paid to do · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
14
05
stay_upright 2, pose 0.1, and head_up 1 shape posture without defining the independent running gate.
06
foot_clearance 0.5, smooth_moves 0.1, plant_the_foot 0.05, no_limit_parking 1, and calm_roll 0.025 are active costs.
Notes: Reward design: what the agent is paid to do · 2/2 stay_upright 2, pose 0.1, and head_up 1 shape posture without defining the independent running gate. foot_clearance 0.5, smooth_moves 0.1, plant_the_foot 0.05, no_limit_parking 1, and calm_roll 0.025 are active costs. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 15
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Recorded training recipe · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
15
01
Base v3: seed 7, 6,000,640 transitions, 16 envs x 128 steps, 2,930 rollouts, 46,880 optimizer minibatches, learning rate 0.0003.
02
Continuation v4: 2,097,152 transitions, 1,024 rollouts, 16,384 optimizer minibatches, learning rate 0.0001.
03
Entire selected lineage: 8,097,792 transitions, 3,954 rollout/update cycles, and 63,264 optimizer minibatches.
04
Both stages use 4 minibatches x 4 epochs, gamma 0.99, GAE lambda 0.95, clip 0.2, value coefficient 1, entropy 0, and max grad norm 0.5.
Notes: Recorded training recipe · 1/2 Base v3: seed 7, 6,000,640 transitions, 16 envs x 128 steps, 2,930 rollouts, 46,880 optimizer minibatches, learning rate 0.0003. Continuation v4: 2,097,152 transitions, 1,024 rollouts, 16,384 optimizer minibatches, learning rate 0.0001. Entire selected lineage: 8,097,792 transitions, 3,954 rollout/update cycles, and 63,264 optimizer minibatches. Both stages use 4 minibatches x 4 epochs, gamma 0.99, GAE lambda 0.95, clip 0.2, value coefficient 1, entropy 0, and max grad norm 0.5. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 16
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Recorded training recipe · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
16
05
Initial std is 0.6 in the base; continuation loads learned actor, critic, log std, observation stats, and reward-return stats but fresh Adam state.
06
Update log fields are phase, steps, seconds, optimizer_steps, mean_loss, policy_loss, value_loss, entropy, approximate_kl, clip_fraction, explained_variance, env_steps.
Notes: Recorded training recipe · 2/2 Initial std is 0.6 in the base; continuation loads learned actor, critic, log std, observation stats, and reward-return stats but fresh Adam state. Update log fields are phase, steps, seconds, optimizer_steps, mean_loss, policy_loss, value_loss, entropy, approximate_kl, clip_fraction, explained_variance, env_steps. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 17
COPYABLE COMMANDS ALSO IN INSTRUCTOR GUIDE / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Hands-on commands: inspect, smoke, train · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
17
01
From .:
./scripts/train-running.sh --dry-run
Inspect the guarded two-stage Running pipeline without training.
02
From .:
./scripts/train-running.sh
Run the independent Full Running base and refinement pipeline with fresh outputs.
Notes: Hands-on commands: inspect, smoke, train · 1/3 From .: ./scripts/train-running.sh --dry-run Inspect the guarded two-stage Running pipeline without training. From .: ./scripts/train-running.sh Run the independent Full Running base and refinement pipeline with fresh outputs. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 18
COPYABLE COMMANDS ALSO IN INSTRUCTOR GUIDE / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Hands-on commands: inspect, smoke, train · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
18
03
From .:
RUN=running-classroom-$(date +%Y%m%d-%H%M%S); ./scripts/train-running.sh --recipe-json docs/remaining-scenarios-e2e/recipes/running.json --init-from rlx/runs/studio/running/running-e2e-20260907-v3/running.safetensors --run-name "$RUN"
Refine the retained v3 checkpoint with its adjacent sidecar in a fresh run; keep RUN in this terminal for the following audit. Requires the ignored historical base artifacts.
04
From .:
rlx/.venv-microduck/bin/python rlx/scripts/audit_scenarios.py --recipe-json docs/remaining-scenarios-e2e/recipes/running.json --run "rlx/runs/studio/running/${RUN:?Run the refinement command first in this shell}" --output "rlx/artifacts/$RUN-audit" --seeds 501 502 503 504 505 --render
Audit a completed Running reproduction over five held-out reset seeds.
Notes: Hands-on commands: inspect, smoke, train · 2/3 From .: RUN=running-classroom-$(date +%Y%m%d-%H%M%S); ./scripts/train-running.sh --recipe-json docs/remaining-scenarios-e2e/recipes/running.json --init-from rlx/runs/studio/running/running-e2e-20260907-v3/running.safetensors --run-name "$RUN" Refine the retained v3 checkpoint with its adjacent sidecar in a fresh run; keep RUN in this terminal for the following audit. Requires the ignored historical base artifacts. From .: rlx/.venv-microduck/bin/python rlx/scripts/audit_scenarios.py --recipe-json docs/remaining-scenarios-e2e/recipes/running.json --run "rlx/runs/studio/running/${RUN:?Run the refinement command first in this shell}" --output "rlx/artifacts/$RUN-audit" --seeds 501 502 503 504 505 --render Audit a completed Running reproduction over five held-out reset seeds. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 19
COPYABLE COMMANDS ALSO IN INSTRUCTOR GUIDE / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Hands-on commands: inspect, smoke, train · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
19
05
From .:
python3 -m unittest discover -s scripts/scenarios -p 'test_*.py'
Run scenario-pipeline unit tests without starting training.
Notes: Hands-on commands: inspect, smoke, train · 3/3 From .: python3 -m unittest discover -s scripts/scenarios -p 'test_*.py' Run scenario-pipeline unit tests without starting training. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 20
MEASURED TRAINING LOGS / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Reward: does the logged signal match the task?
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
20
Training reward is an optimization signal, not the acceptance test. See raw/<case>/ for complete recorded fields.
Notes: Reward: does the logged signal match the task? Chart source: rlx/runs/studio/running/running-e2e-20260907-v4/training-metrics.jsonl Training reward is an optimization signal, not the acceptance test. See raw/<case>/ for complete recorded fields. Series are unsmoothed recorded values. Gaps mean the logger did not provide the requested field. Reward definitions differ: mean_raw_return is episodic, mean_reward is a collection-step mean, and drawing mean_rollout_reward is a rollout-step mean. Do not compare numerical scales across scenarios. No interpolation of missing metrics and no claim of a new experiment. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 21
MEASURED TRAINING LOGS / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Loss: inspect actor, critic and policy drift
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
21
A lower loss does not prove a better robot skill. Loss sign and scale depend on the implementation.
Notes: Loss: inspect actor, critic and policy drift Chart source: rlx/runs/studio/running/running-e2e-20260907-v4/training-metrics.jsonl A lower loss does not prove a better robot skill. Loss sign and scale depend on the implementation. Series are unsmoothed recorded values. Gaps mean the logger did not provide the requested field. Reward definitions differ: mean_raw_return is episodic, mean_reward is a collection-step mean, and drawing mean_rollout_reward is a rollout-step mean. Do not compare numerical scales across scenarios. No interpolation of missing metrics and no claim of a new experiment. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 22
MEASURED TRAINING LOGS / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Diagnostics: is the optimizer behaving?
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
22
Entropy, clipping, explained variance and timing are diagnostics — not a standalone pass/fail certificate.
Notes: Diagnostics: is the optimizer behaving? Chart source: rlx/runs/studio/running/running-e2e-20260907-v4/training-metrics.jsonl Entropy, clipping, explained variance and timing are diagnostics — not a standalone pass/fail certificate. Series are unsmoothed recorded values. Gaps mean the logger did not provide the requested field. Reward definitions differ: mean_raw_return is episodic, mean_reward is a collection-step mean, and drawing mean_rollout_reward is a rollout-step mean. Do not compare numerical scales across scenarios. No interpolation of missing metrics and no claim of a new experiment. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 23
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Metric matrix: numerical audit of this trace · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
23
01
approximate_kl: first 2.824 → final 0.03259; min 0.01741, max 2.824; 1024 logged samples.
02
clip_fraction: first 0.8713 → final 0.3572; min 0.2467, max 0.8713; 1024 logged samples.
03
entropy: first 1.830 → final -0.3148; min -0.3150, max 1.876; 1024 logged samples.
04
explained_variance: first 0.8329 → final 0.6748; min -1.234, max 0.9469; 1024 logged samples.
Notes: Metric matrix: numerical audit of this trace · 1/3 approximate_kl: first 2.824 → final 0.03259; min 0.01741, max 2.824; 1024 logged samples. clip_fraction: first 0.8713 → final 0.3572; min 0.2467, max 0.8713; 1024 logged samples. entropy: first 1.830 → final -0.3148; min -0.3150, max 1.876; 1024 logged samples. explained_variance: first 0.8329 → final 0.6748; min -1.234, max 0.9469; 1024 logged samples. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 24
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Metric matrix: numerical audit of this trace · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
24
05
mean_loss: first 0.1724 → final -0.02380; min -0.03384, max 0.1724; 1024 logged samples.
06
mean_raw_return: first 8637 → final 9686; min 87.22, max 1.008e+4; 1738 logged samples.
07
mean_reward: first 0.03103 → final 0.03508; min 0.02922, max 0.03661; 1024 logged samples.
08
policy_loss: first 0.1711 → final -0.02410; min -0.03457, max 0.1711; 1024 logged samples.
Notes: Metric matrix: numerical audit of this trace · 2/3 mean_loss: first 0.1724 → final -0.02380; min -0.03384, max 0.1724; 1024 logged samples. mean_raw_return: first 8637 → final 9686; min 87.22, max 1.008e+4; 1738 logged samples. mean_reward: first 0.03103 → final 0.03508; min 0.02922, max 0.03661; 1024 logged samples. policy_loss: first 0.1711 → final -0.02410; min -0.03457, max 0.1711; 1024 logged samples. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 25
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Metric matrix: numerical audit of this trace · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
25
09
value_loss: first 0.001326 → final 0.0003019; min 0.0002014, max 0.01952; 1024 logged samples.
Notes: Metric matrix: numerical audit of this trace · 3/3 value_loss: first 0.001326 → final 0.0003019; min 0.0002014, max 0.01952; 1024 logged samples. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 26
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Verification: define success before looking · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
26
01
Require every episode to complete 600 samples without termination, with finite physical metrics and upright fraction >= 0.95.
02
Require commanded fraction >= 0.50, mean directed speed >= 0.35 m/s, signed intended displacement >= 2.0 m, and speed ratio >= 0.35.
03
Require at least 8 alternating exclusive-support switches, each foot air fraction >= 0.08, contact fraction >= 0.10, and lift/touch events.
04
Require both-feet aerial fraction >= 0.03; this distinguishes running from fast grounded stepping.
Notes: Verification: define success before looking · 1/2 Require every episode to complete 600 samples without termination, with finite physical metrics and upright fraction >= 0.95. Require commanded fraction >= 0.50, mean directed speed >= 0.35 m/s, signed intended displacement >= 2.0 m, and speed ratio >= 0.35. Require at least 8 alternating exclusive-support switches, each foot air fraction >= 0.08, contact fraction >= 0.10, and lift/touch events. Require both-feet aerial fraction >= 0.03; this distinguishes running from fast grounded stepping. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 27
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Verification: define success before looking · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
27
05
Use evaluator version 2 signed displacement, which anchors intended heading at command changes and advances it only by commanded yaw.
06
Require zero, random, and loaded initial controls to fail the final gate; verify hashes, finite telemetry, 61-to-14 ONNX, parity, and video.
Notes: Verification: define success before looking · 2/2 Use evaluator version 2 signed displacement, which anchors intended heading at command changes and advances it only by commanded yaw. Require zero, random, and loaded initial controls to fail the final gate; verify hashes, finite telemetry, 61-to-14 ONNX, parity, and video. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 28
SAVED RESULTS — NOT A NEW TRAINING RUN / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Results: what was actually measured · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
28
01
Actual final evidence: PASS for running-e2e-20260907-v4; Studio evaluation passed 16/16 complete 12-second episodes.
02
Independent seeds 501-505 passed 5/5; directed speeds were 0.7382723265470258-0.7746384824233077 m/s.
03
Signed intended displacement was 3.8483205827178626-9.01295603365732 m; speed ratios were 0.9843631020627012-1.0328513098977434.
04
Aerial fractions were 0.35-0.3983333333333333, with 167-170 support switches; every episode had upright fraction 1.0.
Notes: Results: what was actually measured · 1/3 Actual final evidence: PASS for running-e2e-20260907-v4; Studio evaluation passed 16/16 complete 12-second episodes. Independent seeds 501-505 passed 5/5; directed speeds were 0.7382723265470258-0.7746384824233077 m/s. Signed intended displacement was 3.8483205827178626-9.01295603365732 m; speed ratios were 0.9843631020627012-1.0328513098977434. Aerial fractions were 0.35-0.3983333333333333, with 167-170 support switches; every episode had upright fraction 1.0. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 29
SAVED RESULTS — NOT A NEW TRAINING RUN / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Results: what was actually measured · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
29
05
The v3 initializer was already aerial at fraction 0.275 with 156 switches and 0.6664 m/s, but failed with -0.2392 m intended displacement.
06
After 524,288 continuation transitions, comparison seed 501 passed; the final checkpoint retained a pass with raw return 11467.54.
07
Final raw-return change versus initialization was 1683.1782192444243; learned tensor L2 change was 7.672545078668774.
08
ONNX/native maximum action error was 1.430511474609375e-6; zero and random controls fell after 43-49 steps and failed the gate.
Notes: Results: what was actually measured · 2/3 The v3 initializer was already aerial at fraction 0.275 with 156 switches and 0.6664 m/s, but failed with -0.2392 m intended displacement. After 524,288 continuation transitions, comparison seed 501 passed; the final checkpoint retained a pass with raw return 11467.54. Final raw-return change versus initialization was 1683.1782192444243; learned tensor L2 change was 7.672545078668774. ONNX/native maximum action error was 1.430511474609375e-6; zero and random controls fell after 43-49 steps and failed the gate. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 30
SAVED RESULTS — NOT A NEW TRAINING RUN / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Results: what was actually measured · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
30
09
Final-100 means: policy_loss -0.022870965473121032, value_loss 0.0003489635748883302, mean_loss -0.022522001879488017.
10
Final-100 approximate_kl 0.03082194794646057, clip_fraction 0.33925048828125, explained_variance 0.5853159072389115.
Notes: Results: what was actually measured · 3/3 Final-100 means: policy_loss -0.022870965473121032, value_loss 0.0003489635748883302, mean_loss -0.022522001879488017. Final-100 approximate_kl 0.03082194794646057, clip_fraction 0.33925048828125, explained_variance 0.5853159072389115. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 31
EMBEDDED OFFLINE VIDEO / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Watch the actual saved rollout
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
31
BEFORE PLAY
Predict one success signal and one failure signal.
AFTER PLAY
Which claims does this clip support? What remains untested?
12.0 s saved MP4 • Click in PowerPoint Slide Show • Backup: videos/running-rollout.mp4
Notes: Saved policy video Source: rlx/runs/studio/running/running-e2e-20260907-v4/render/ep0.mp4 Embedded video bytes are copied unchanged, not regenerated and not sped up. A single video is not a seed sweep. PowerPoint playback requires a user click; use the included MP4 in a local player if a presentation viewer cannot decode embedded media. The policy specializes to one nominal 0.75 m/s forward command; arbitrary speed, turning, and disturbance recovery are untested. The passing paths still curve; the result proves signed intended progress under the gate, not straight-line path perfection. The base acquired running, while v4 improved intended progress; crediting v4 with discovering the entire gait would be inaccurate. Raw actor means can exceed the applied [-4,4] target-offset range, so nominal XML success is not a hardware command-quality certificate. No BAM dynamics, current limits, latency, randomized physics, terrain, pushes, battery, thermal, cable, backlash, or hardware safety tests. One training lineage and five nominal audit seeds do not establish training-seed robustness or broad generalization. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 32
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Limits and failure analysis · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
32
01
The policy specializes to one nominal 0.75 m/s forward command; arbitrary speed, turning, and disturbance recovery are untested.
02
The passing paths still curve; the result proves signed intended progress under the gate, not straight-line path perfection.
03
The base acquired running, while v4 improved intended progress; crediting v4 with discovering the entire gait would be inaccurate.
04
Raw actor means can exceed the applied [-4,4] target-offset range, so nominal XML success is not a hardware command-quality certificate.
Notes: Limits and failure analysis · 1/2 The policy specializes to one nominal 0.75 m/s forward command; arbitrary speed, turning, and disturbance recovery are untested. The passing paths still curve; the result proves signed intended progress under the gate, not straight-line path perfection. The base acquired running, while v4 improved intended progress; crediting v4 with discovering the entire gait would be inaccurate. Raw actor means can exceed the applied [-4,4] target-offset range, so nominal XML success is not a hardware command-quality certificate. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 33
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Limits and failure analysis · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
33
05
No BAM dynamics, current limits, latency, randomized physics, terrain, pushes, battery, thermal, cable, backlash, or hardware safety tests.
06
One training lineage and five nominal audit seeds do not establish training-seed robustness or broad generalization.
Notes: Limits and failure analysis · 2/2 No BAM dynamics, current limits, latency, randomized physics, terrain, pushes, battery, thermal, cable, backlash, or hardware safety tests. One training lineage and five nominal audit seeds do not establish training-seed robustness or broad generalization. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 34
PROPOSED PRACTICE — NOT MEASURED RESULTS / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Student lab: change one variable, keep the gates · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
34
01
Recommended exercise, not saved evidence: classify a 0.72 m/s gait with aerial fraction 0.01 against the exact running gate.
02
Recommended exercise, not saved evidence: identify observable yaw-rate inputs and explain why absolute-heading reward is invalid.
03
Recommended exercise, not saved evidence: clip the recorded first raw actor vector and list saturated joints.
04
Recommended exercise, not saved evidence: construct a circular trajectory with high body-frame speed but near-zero intended displacement.
Notes: Student lab: change one variable, keep the gates · 1/2 Recommended exercise, not saved evidence: classify a 0.72 m/s gait with aerial fraction 0.01 against the exact running gate. Recommended exercise, not saved evidence: identify observable yaw-rate inputs and explain why absolute-heading reward is invalid. Recommended exercise, not saved evidence: clip the recorded first raw actor vector and list saturated joints. Recommended exercise, not saved evidence: construct a circular trajectory with high body-frame speed but near-zero intended displacement. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 35
PROPOSED PRACTICE — NOT MEASURED RESULTS / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Student lab: change one variable, keep the gates · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
35
05
Recommended exercise, not saved evidence: predeclare held-out speed and yaw-rate commands for interpolation and extrapolation tests.
Notes: Student lab: change one variable, keep the gates · 2/2 Recommended exercise, not saved evidence: predeclare held-out speed and yaw-rate commands for interpolation and extrapolation tests. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 36
PPO ROBOTICS LAB / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Submit an experiment, not just a video
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
36
01
Before training: write one hypothesis, the changed parameter, the fixed baseline, seed list, acceptance criteria and time/transition budget.
02
During training: save the exact command, environment versions, initialization, checkpoint and raw reward/loss/KL metrics. Never overwrite the saved reference run.
03
After training: evaluate the frozen exported policy on matched seeds; include all failures, aggregate metrics, the full rollout video and a source-bound result table.
04
Rubric / 10: reproducibility 2; environment and reward explanation 2; PPO and metrics interpretation 2; honest verification 2; one evidence-based next experiment 2.
Notes: Submit an experiment, not just a video Before training: write one hypothesis, the changed parameter, the fixed baseline, seed list, acceptance criteria and time/transition budget. During training: save the exact command, environment versions, initialization, checkpoint and raw reward/loss/KL metrics. Never overwrite the saved reference run. After training: evaluate the frozen exported policy on matched seeds; include all failures, aggregate metrics, the full rollout video and a source-bound result table. Rubric / 10: reproducibility 2; environment and reward explanation 2; PPO and metrics interpretation 2; honest verification 2; one evidence-based next experiment 2. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 37
REPOSITORY-RELATIVE PATHS / FULL SOURCES IN NOTES / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Source map and further study · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
37
01
AGENTS.md
02
microduck_local/AGENTS.md
03
microduck_local/src/microduck_local/contract.py
04
README.md
Notes: Source map and further study · 1/2 AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 38
REPOSITORY-RELATIVE PATHS / FULL SOURCES IN NOTES / RUNNING: AERIAL GAIT WITH INTENDED PROGRESS
Source map and further study · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
38
05
docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md
06
docs/microduck-training-student-book/chapters/02b-gae-workshop.md
07
scripts/scenarios/README.md
08
README.md
Notes: Source map and further study · 2/2 docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): AGENTS.md microduck_local/AGENTS.md microduck_local/src/microduck_local/contract.py README.md rlx/README.md scripts/train-running.sh scripts/scenarios/README.md docs/microduck-training-student-book/chapters/06-running.md docs/microduck-training-student-book/REPRODUCTION.md docs/remaining-scenarios-e2e/REPORT.md docs/remaining-scenarios-e2e/recipes/running-base.json docs/remaining-scenarios-e2e/recipes/running.json rlx/rlx/environments/microduck_recipes.py rlx/scripts/audit_scenarios.py rlx/runs/studio/running/running-e2e-20260907-v4/running.safetensors.json rlx/runs/studio/running/running-e2e-20260907-v4/evaluation.json rlx/runs/studio/running/running-e2e-20260907-v4/render/evidence.json rlx/artifacts/scenarios-e2e-20260907/running-v4-audit/audit.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/running/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.