## Slide 1
EIGHT CASES / ONE LEARNING METHOD / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
LAB 05
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
01
Assisted backflip
Backflip: Assisted Launch, PPO Landing, and Stand Handoff
Environment design · PPO · Honest verification
BUILD → TRAIN → VERIFY → EXPLAIN
Notes: Backflip: Assisted Launch, PPO Landing, and Stand Handoff Use case: Teach controller ownership, transfer learning, PPO diagnostics, and evidence boundaries through a three-stage simulated backflip. The spotter owns launch energy and rotation, the trained PPO actor owns only the landing window, and the pretrained stand policy owns the final hold. Start by explaining the difference between a simulation training pipeline and skill mastery. The cover image is a frame decoded from this case's actual rollout, not generated artwork. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 2
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
What you will build — and what the evidence says
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
02
01
Use case: Teach controller ownership, transfer learning, PPO diagnostics, and evidence boundaries through a three-stage simulated backflip. The spotter owns launch energy and rotation, the trained PPO actor owns only the landing window, and the pretrained stand policy owns the final hold.
02
By the end: describe the scene, map observations to actions, explain the reward, trace one PPO update, run a bounded experiment, and defend an evaluation claim.
03
This is not an unassisted learned backflip. The simulator spotter supplies substantial launch energy and rotation.
04
Scope: local MuJoCo simulation. Do not deploy these classroom artifacts to a physical robot; hardware transfer requires a separate validated process.
Notes: What you will build — and what the evidence says Use case: Teach controller ownership, transfer learning, PPO diagnostics, and evidence boundaries through a three-stage simulated backflip. The spotter owns launch energy and rotation, the trained PPO actor owns only the landing window, and the pretrained stand policy owns the final hold. By the end: describe the scene, map observations to actions, explain the reward, trace one PPO update, run a bounded experiment, and defend an evaluation claim. This is not an unassisted learned backflip. The simulator spotter supplies substantial launch energy and rotation. Scope: local MuJoCo simulation. Do not deploy these classroom artifacts to a physical robot; hardware transfer requires a separate validated process. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 3
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Materials and prerequisites · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
03
01
Microduck MuJoCo model with XML position servos at 50 Hz control
02
microduck/policies/alpha_stand.onnx as the exact actor and observation-normalizer source and as the post-landing stand controller
03
rlx/rlx/environments/backflip.py for the assisted launch, landing-only reward, stage metrics, and handoff logic
04
rlx/rlx/environments/backflip_evaluation.py for the independent physical acceptance gate
Notes: Materials and prerequisites · 1/2 Microduck MuJoCo model with XML position servos at 50 Hz control microduck/policies/alpha_stand.onnx as the exact actor and observation-normalizer source and as the post-landing stand controller rlx/rlx/environments/backflip.py for the assisted launch, landing-only reward, stage metrics, and handoff logic rlx/rlx/environments/backflip_evaluation.py for the independent physical acceptance gate Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 4
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Materials and prerequisites · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
04
05
rlx/rlx/models/backflip_bootstrap.py for exact teacher transfer, parity checks, reward calibration, and critic fitting
06
rlx/examples/ppo_microduck_studio.py and scripts/train-backflip.sh for training, evaluation, rendering, and export
07
rlx/runs/studio/backflip/backflip-e2e-20260908-v5/ for the retained trained run
08
rlx/artifacts/backflip-e2e-20260908-v5/ for the independent audit, plots, per-seed arrays, and provenance
Notes: Materials and prerequisites · 2/2 rlx/rlx/models/backflip_bootstrap.py for exact teacher transfer, parity checks, reward calibration, and critic fitting rlx/examples/ppo_microduck_studio.py and scripts/train-backflip.sh for training, evaluation, rendering, and export rlx/runs/studio/backflip/backflip-e2e-20260908-v5/ for the retained trained run rlx/artifacts/backflip-e2e-20260908-v5/ for the independent audit, plots, per-seed arrays, and provenance Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 5
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Environment and policy contract · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
05
01
Simulation only. Protocol spotter-launch-landing-stand-v2 uses explicit MuJoCo generalized external forces during launch; it does not teleport the robot.
02
Control contract: float32 observation shape 61 and action shape 14 at 50 Hz. Actions are 14 joint-target offsets in the fixed servo order.
03
Observation indices 0:3 are trunk angular velocity; 3:6 projected gravity; 6:20 joint position offsets; 20:34 one-control-step-lagged joint velocity; 34:48 previous raw action; 48:51 twist command; 51:55 head command; 55:61 body command.
04
The landing actor receives no extra stage, phase, world position, yaw, launch-force, or contact channel. Composite controller code knows the stage, but the PPO actor still receives the standard 61 values.
Notes: Environment and policy contract · 1/3 Simulation only. Protocol spotter-launch-landing-stand-v2 uses explicit MuJoCo generalized external forces during launch; it does not teleport the robot. Control contract: float32 observation shape 61 and action shape 14 at 50 Hz. Actions are 14 joint-target offsets in the fixed servo order. Observation indices 0:3 are trunk angular velocity; 3:6 projected gravity; 6:20 joint position offsets; 20:34 one-control-step-lagged joint velocity; 34:48 previous raw action; 48:51 twist command; 51:55 head command; 55:61 body command. The landing actor receives no extra stage, phase, world position, yaw, launch-force, or contact channel. Composite controller code knows the stage, but the PPO actor still receives the standard 61 values. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 6
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Environment and policy contract · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
06
05
Launch duration is 1.2 s. The pitch target ends at 5.3 rad with target rate 5 rad/s; target height rises to 0.32 m and lowers toward 0.22 m before release.
06
Launch gains and clamps are pitch kp 1.5, pitch kd 0.24, pitch torque limit 1.3 Nm, vertical kp 90, vertical kd 8.5, vertical force limit 15 N, lateral damping 3, and roll/yaw damping 0.1.
07
Release must reach at least 5.3 rad with backward angular speed between 3.5 and 6.5 rad/s. All external forces and torques are cleared at release.
08
Handoff requires at least 5.8 rad credited rotation and 10 consecutive stable PPO samples: both feet supported, no non-foot support, upright projection at least 0.9, trunk height at least 0.105 m, gyro norm below sqrt(2) rad/s, and no spotter assistance.
Notes: Environment and policy contract · 2/3 Launch duration is 1.2 s. The pitch target ends at 5.3 rad with target rate 5 rad/s; target height rises to 0.32 m and lowers toward 0.22 m before release. Launch gains and clamps are pitch kp 1.5, pitch kd 0.24, pitch torque limit 1.3 Nm, vertical kp 90, vertical kd 8.5, vertical force limit 15 N, lateral damping 3, and roll/yaw damping 0.1. Release must reach at least 5.3 rad with backward angular speed between 3.5 and 6.5 rad/s. All external forces and torques are cleared at release. Handoff requires at least 5.8 rad credited rotation and 10 consecutive stable PPO samples: both feet supported, no non-foot support, upright projection at least 0.9, trunk height at least 0.105 m, gyro norm below sqrt(2) rad/s, and no spotter assistance. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 7
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Environment and policy contract · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
07
09
After handoff, alpha_stand.onnx must maintain the final 100 consecutive stable samples, equal to 2 s at 50 Hz.
Notes: Environment and policy contract · 3/3 After handoff, alpha_stand.onnx must maintain the final 100 consecutive stable samples, equal to 2 s at 50 Hz. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 8
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
How this case is built: one evidence loop
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
08
01 / SCENE
Ground + spotter launch
02 / INITIALIZE
Prior policy + calibration
03 / PPO
Train landing phase
04 / HANDOFF
Pretrained standing policy
05 / VERIFY
No teleport; gate each phase
06 / EVIDENCE
Assisted result, not free flip
Failure is data: change one cause, retrain, and repeat the same evaluation gates.
Notes: Case-specific build flow 01 / SCENE: Ground + spotter launch 02 / INITIALIZE: Prior policy + calibration 03 / PPO: Train landing phase 04 / HANDOFF: Pretrained standing policy 05 / VERIFY: No teleport; gate each phase 06 / EVIDENCE: Assisted result, not free flip This is an explanatory workflow diagram, not a measured learning curve. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 9
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Build the case step by step · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
09
01
Start with the invariant 61-observation/14-action contract and label which signals the landing actor can actually observe.
02
Load alpha_stand.onnx and verify its 512-256-128 ELU actor structure, 61 inputs, 14 outputs, and observation normalizer before transfer.
03
Collect 16 teacher landing episodes of 600 steps each, producing 9,600 calibration samples from assisted-release states.
04
Copy the teacher actor and normalizer exactly, require action parity below 1e-4, and freeze observation normalization.
Notes: Build the case step by step · 1/3 Start with the invariant 61-observation/14-action contract and label which signals the landing actor can actually observe. Load alpha_stand.onnx and verify its 512-256-128 ELU actor structure, 61 inputs, 14 outputs, and observation normalizer before transfer. Collect 16 teacher landing episodes of 600 steps each, producing 9,600 calibration samples from assisted-release states. Copy the teacher actor and normalizer exactly, require action parity below 1e-4, and freeze observation normalization. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 10
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Build the case step by step · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
10
05
Fit only the fresh critic for 10 epochs with Adam at 3e-4; keep the transferred actor unchanged during this calibration.
06
Reset each training episode through the assisted launch, then expose the release observation to PPO. Assisted preparation steps are outside the PPO transition count and receive zero PPO reward.
07
Train only the landing actor. Do not run a stand-policy override during PPO collection.
08
Evaluate the complete three-stage controller with deterministic actions and reconstruct the pre-handoff stability streak independently.
Notes: Build the case step by step · 2/3 Fit only the fresh critic for 10 epochs with Adam at 3e-4; keep the transferred actor unchanged during this calibration. Reset each training episode through the assisted launch, then expose the release observation to PPO. Assisted preparation steps are outside the PPO transition count and receive zero PPO reward. Train only the landing actor. Do not run a stand-policy override during PPO collection. Evaluate the complete three-stage controller with deterministic actions and reconstruct the pre-handoff stability streak independently. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 11
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Build the case step by step · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
11
09
Run the landing-only audit with the stand handoff removed so the PPO actor must hold the final 100 samples itself.
10
Compare the final actor against the exact initializer and zero-action control on paired seeds; do not infer learning from showcase success.
11
Render the stage-labeled MP4 and contact sheet, then verify policy, stand-policy, evaluation, and media hashes before using the clip.
Notes: Build the case step by step · 3/3 Run the landing-only audit with the stand handoff removed so the PPO actor must hold the final 100 samples itself. Compare the final actor against the exact initializer and zero-action control on paired seeds; do not infer learning from showcase success. Render the stage-labeled MP4 and contact sheet, then verify policy, stand-policy, evaluation, and media hashes before using the clip. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 12
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
PPO: improve the actor without trusting a huge step
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
12
ratio = πnew(a | o) / πold(a | o)
Maximize mean[min(ratio × A, clip(ratio, 1 − ε, 1 + ε) × A)]
Actor: chooses joint actions. Critic: estimates future discounted reward.
A = advantage. ε = clipping range. Old log probabilities stay fixed for each collected batch.
Notes: PPO clipped surrogate This is a teaching formula, not a saved experiment value. The optimizer minimizes the negative policy surrogate plus the implementation-specific value and entropy terms. PPO clipping is not a hard KL bound; monitor KL and clip fraction. A negative policy loss or Gaussian entropy is not automatically an error. Each scenario has its own reward units and optimizer conventions. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 13
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Follow one rollout through the learner
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
13
01
Collect observations, sampled actions, old log probabilities, values, rewards and episode-boundary flags using the current stochastic actor.
02
Compute TD residuals and generalized advantage estimates (GAE). A true terminal has zero continuation value; a timeout may bootstrap the saved final observation.
03
Cut advantage traces at reset boundaries. Never bootstrap a timeout from the first observation of the next episode.
04
Reuse this batch for PPO minibatch updates, then collect fresh on-policy data. Export the deterministic actor and its observation transform for evaluation.
Notes: Follow one rollout through the learner Collect observations, sampled actions, old log probabilities, values, rewards and episode-boundary flags using the current stochastic actor. Compute TD residuals and generalized advantage estimates (GAE). A true terminal has zero continuation value; a timeout may bootstrap the saved final observation. Cut advantage traces at reset boundaries. Never bootstrap a timeout from the first observation of the next episode. Reuse this batch for PPO minibatch updates, then collect fresh on-policy data. Export the deterministic actor and its observation transform for evaluation. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 14
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Paper exercise: count samples and clip the objective
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
14
01
Illustrative arithmetic, NOT this run: 16 environments × 128 steps = 2,048 fresh transitions per rollout. Four epochs reuse those transitions; they do not create 8,192 new samples.
02
With ε = 0.2, ratio = 1.4 and A = +2: min(2.8, 2.4) = 2.4. The minimized policy term is −2.4 before averaging and additional loss terms.
03
With the same ratio and A = −2: min(−2.8, −2.4) = −2.8. Explain why clipping is asymmetric once the sign of the advantage changes.
04
Run from repo root: python3 docs/microduck-training-student-book/learning_lab.py --gae. This is a deterministic arithmetic lab, not new policy training.
Notes: Paper exercise: count samples and clip the objective Illustrative arithmetic, NOT this run: 16 environments × 128 steps = 2,048 fresh transitions per rollout. Four epochs reuse those transitions; they do not create 8,192 new samples. With ε = 0.2, ratio = 1.4 and A = +2: min(2.8, 2.4) = 2.4. The minimized policy term is −2.4 before averaging and additional loss terms. With the same ratio and A = −2: min(−2.8, −2.4) = −2.8. Explain why clipping is asymmetric once the sign of the advantage changes. Run from repo root: python3 docs/microduck-training-student-book/learning_lab.py --gae. This is a deterministic arithmetic lab, not new policy training. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 15
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Reward design: what the agent is paid to do · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
15
01
name: landing_upright | weight: 3 | sign: reward | definition: clip((1 - projected_gravity_z) / 2, 0, 1) | scope: PPO landing stage only
02
name: landing_pose | weight: 2 | sign: reward | definition: landing_upright times the mean of equal 0.60-rad and 0.15-rad Gaussian pose kernels | scope: PPO landing stage only
03
name: landing_settle | weight: 1 | sign: reward | definition: landing_upright times pose score times exp(-sum(gyro squared) / 2) | scope: PPO landing stage only
04
name: landing_joint_speed_penalty | weight: 0.05 | sign: penalty | definition: -mean(min(joint_velocity squared / 100, 1)) | scope: PPO landing stage only
Notes: Reward design: what the agent is paid to do · 1/2 name: landing_upright | weight: 3 | sign: reward | definition: clip((1 - projected_gravity_z) / 2, 0, 1) | scope: PPO landing stage only name: landing_pose | weight: 2 | sign: reward | definition: landing_upright times the mean of equal 0.60-rad and 0.15-rad Gaussian pose kernels | scope: PPO landing stage only name: landing_settle | weight: 1 | sign: reward | definition: landing_upright times pose score times exp(-sum(gyro squared) / 2) | scope: PPO landing stage only name: landing_joint_speed_penalty | weight: 0.05 | sign: penalty | definition: -mean(min(joint_velocity squared / 100, 1)) | scope: PPO landing stage only Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 16
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Reward design: what the agent is paid to do · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
16
05
name: landing_action_rate_penalty | weight: 0.02 | sign: penalty | definition: -mean(min((action - previous_action) squared, 1)) | scope: PPO landing stage only
06
name: landing_action_size_penalty | weight: 0.01 | sign: penalty | definition: -mean(min(action squared / 16, 1)) | scope: PPO landing stage only
07
name: total_reward | weight: null | sign: bounded sum | definition: 3*landing_upright + 2*landing_pose + landing_settle + 0.05*landing_joint_speed_penalty + 0.02*landing_action_rate_penalty + 0.01*landing_action_size_penalty; bounded from -0.08 to 6 | scope: Every component is zero during assisted launch and pretrained stand handoff
Notes: Reward design: what the agent is paid to do · 2/2 name: landing_action_rate_penalty | weight: 0.02 | sign: penalty | definition: -mean(min((action - previous_action) squared, 1)) | scope: PPO landing stage only name: landing_action_size_penalty | weight: 0.01 | sign: penalty | definition: -mean(min(action squared / 16, 1)) | scope: PPO landing stage only name: total_reward | weight: null | sign: bounded sum | definition: 3*landing_upright + 2*landing_pose + landing_settle + 0.05*landing_joint_speed_penalty + 0.02*landing_action_rate_penalty + 0.01*landing_action_size_penalty; bounded from -0.08 to 6 | scope: Every component is zero during assisted launch and pretrained stand handoff Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 17
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Recorded training recipe · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
17
01
config: transition_budget | value: 401408 | detail: 196 complete batches of 16 environments x 128 steps; assisted reset preparation is excluded
02
config: ppo_batch | value: 16 environments, 128 steps per environment, 4 minibatches, 2 update epochs
03
config: optimizer | value: Adam learning rate 3e-6, maximum gradient norm 0.5, fresh PPO optimizer
04
config: discount_and_objective | value: gamma 0.99, GAE lambda 0.95, clip coefficient 0.2, clipped value loss enabled, value coefficient 1.0, normalized advantages enabled
Notes: Recorded training recipe · 1/2 config: transition_budget | value: 401408 | detail: 196 complete batches of 16 environments x 128 steps; assisted reset preparation is excluded config: ppo_batch | value: 16 environments, 128 steps per environment, 4 minibatches, 2 update epochs config: optimizer | value: Adam learning rate 3e-6, maximum gradient norm 0.5, fresh PPO optimizer config: discount_and_objective | value: gamma 0.99, GAE lambda 0.95, clip coefficient 0.2, clipped value loss enabled, value coefficient 1.0, normalized advantages enabled Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 18
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Recorded training recipe · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
18
05
config: exploration | value: initial action standard deviation 0.03, entropy coefficient 0
06
config: normalization | value: transferred observation normalization frozen; reward normalization enabled and frozen after teacher calibration; calibrated discounted-return standard deviation 147.2994092878347
07
config: episode_and_randomization | value: 12 s episodes, seed 7, XML actuator, dummy vector backend, domain randomization off, observation noise off, action delay off, random yaw off
08
config: telemetry_fields | value: phase; env_steps; steps; seconds; optimizer_steps; mean_loss; policy_loss; value_loss; entropy; approximate_kl; clip_fraction; explained_variance; mean_reward; mean_raw_return
Notes: Recorded training recipe · 2/2 config: exploration | value: initial action standard deviation 0.03, entropy coefficient 0 config: normalization | value: transferred observation normalization frozen; reward normalization enabled and frozen after teacher calibration; calibrated discounted-return standard deviation 147.2994092878347 config: episode_and_randomization | value: 12 s episodes, seed 7, XML actuator, dummy vector backend, domain randomization off, observation noise off, action delay off, random yaw off config: telemetry_fields | value: phase; env_steps; steps; seconds; optimizer_steps; mean_loss; policy_loss; value_loss; entropy; approximate_kl; clip_fraction; explained_variance; mean_reward; mean_raw_return Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 19
COPYABLE COMMANDS ALSO IN INSTRUCTOR GUIDE / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Hands-on commands: inspect, smoke, train · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
19
01
From duck-viewer:
npm run dev
Start the Studio service before the API reproduction driver.
02
From duck-viewer:
node scripts/rlx-dance-api-e2e.mjs --execute --experiment backflip --run backflip-reproduction-001 --profile full --recipe-json ../docs/backflip-showcase/recipe.json --report ../.restart-lab/backflip-reproduction-001.json
Run the documented full Studio train, evaluate, render, and export sequence with a fresh run name.
Notes: Hands-on commands: inspect, smoke, train · 1/2 From duck-viewer: npm run dev Start the Studio service before the API reproduction driver. From duck-viewer: node scripts/rlx-dance-api-e2e.mjs --execute --experiment backflip --run backflip-reproduction-001 --profile full --recipe-json ../docs/backflip-showcase/recipe.json --report ../.restart-lab/backflip-reproduction-001.json Run the documented full Studio train, evaluate, render, and export sequence with a fresh run name. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 20
COPYABLE COMMANDS ALSO IN INSTRUCTOR GUIDE / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Hands-on commands: inspect, smoke, train · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
20
03
From .:
rlx/.venv-microduck/bin/python rlx/scripts/audit_backflip.py --run rlx/runs/studio/backflip/backflip-reproduction-001 --output rlx/artifacts/backflip-reproduction-001 --seeds 101,102,103,104,105,106,107,108
Run the paired showcase, landing-only, initializer, stand, and zero-action audit.
04
From duck-viewer:
BACKFLIP_RUN=backflip-e2e-20260908-v5 node scripts/verify-backflip-studio.mjs
Verify the retained V5 Studio card, guidance, evaluation panel, source-bound video, and responsive layout without retraining.
Notes: Hands-on commands: inspect, smoke, train · 2/2 From .: rlx/.venv-microduck/bin/python rlx/scripts/audit_backflip.py --run rlx/runs/studio/backflip/backflip-reproduction-001 --output rlx/artifacts/backflip-reproduction-001 --seeds 101,102,103,104,105,106,107,108 Run the paired showcase, landing-only, initializer, stand, and zero-action audit. From duck-viewer: BACKFLIP_RUN=backflip-e2e-20260908-v5 node scripts/verify-backflip-studio.mjs Verify the retained V5 Studio card, guidance, evaluation panel, source-bound video, and responsive layout without retraining. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 21
MEASURED TRAINING LOGS / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Reward: does the logged signal match the task?
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
21
Training reward is an optimization signal, not the acceptance test. See raw/<case>/ for complete recorded fields.
Notes: Reward: does the logged signal match the task? Chart source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl Training reward is an optimization signal, not the acceptance test. See raw/<case>/ for complete recorded fields. Series are unsmoothed recorded values. Gaps mean the logger did not provide the requested field. Reward definitions differ: mean_raw_return is episodic, mean_reward is a collection-step mean, and drawing mean_rollout_reward is a rollout-step mean. Do not compare numerical scales across scenarios. No interpolation of missing metrics and no claim of a new experiment. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 22
MEASURED TRAINING LOGS / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Loss: inspect actor, critic and policy drift
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
22
A lower loss does not prove a better robot skill. Loss sign and scale depend on the implementation.
Notes: Loss: inspect actor, critic and policy drift Chart source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl A lower loss does not prove a better robot skill. Loss sign and scale depend on the implementation. Series are unsmoothed recorded values. Gaps mean the logger did not provide the requested field. Reward definitions differ: mean_raw_return is episodic, mean_reward is a collection-step mean, and drawing mean_rollout_reward is a rollout-step mean. Do not compare numerical scales across scenarios. No interpolation of missing metrics and no claim of a new experiment. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 23
MEASURED TRAINING LOGS / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Diagnostics: is the optimizer behaving?
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
23
Entropy, clipping, explained variance and timing are diagnostics — not a standalone pass/fail certificate.
Notes: Diagnostics: is the optimizer behaving? Chart source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl Entropy, clipping, explained variance and timing are diagnostics — not a standalone pass/fail certificate. Series are unsmoothed recorded values. Gaps mean the logger did not provide the requested field. Reward definitions differ: mean_raw_return is episodic, mean_reward is a collection-step mean, and drawing mean_rollout_reward is a rollout-step mean. Do not compare numerical scales across scenarios. No interpolation of missing metrics and no claim of a new experiment. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 24
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Metric matrix: numerical audit of this trace · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
24
01
approximate_kl: first 0.04450 → final 0.004050; min 0.001318, max 0.04450; 196 logged samples.
02
clip_fraction: first 0.2825 → final 0.04956; min 0.004150, max 0.2825; 196 logged samples.
03
entropy: first -29.23 → final -29.23; min -29.23, max -29.23; 196 logged samples.
04
explained_variance: first 0.6132 → final 0.9215; min -0.8016, max 0.9343; 196 logged samples.
Notes: Metric matrix: numerical audit of this trace · 1/3 approximate_kl: first 0.04450 → final 0.004050; min 0.001318, max 0.04450; 196 logged samples. clip_fraction: first 0.2825 → final 0.04956; min 0.004150, max 0.2825; 196 logged samples. entropy: first -29.23 → final -29.23; min -29.23, max -29.23; 196 logged samples. explained_variance: first 0.6132 → final 0.9215; min -0.8016, max 0.9343; 196 logged samples. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 25
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Metric matrix: numerical audit of this trace · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
25
05
mean_loss: first 0.001169 → final -0.003597; min -0.01114, max 0.007229; 196 logged samples.
06
mean_raw_return: first 3411 → final 2976; min 2976, max 3411; 41 logged samples.
07
mean_reward: first 0.03612 → final 0.03421; min 0.03213, max 0.03926; 196 logged samples.
08
policy_loss: first -0.0009842 → final -0.003618; min -0.01235, max 0.005976; 196 logged samples.
Notes: Metric matrix: numerical audit of this trace · 2/3 mean_loss: first 0.001169 → final -0.003597; min -0.01114, max 0.007229; 196 logged samples. mean_raw_return: first 3411 → final 2976; min 2976, max 3411; 41 logged samples. mean_reward: first 0.03612 → final 0.03421; min 0.03213, max 0.03926; 196 logged samples. policy_loss: first -0.0009842 → final -0.003618; min -0.01235, max 0.005976; 196 logged samples. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 26
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Metric matrix: numerical audit of this trace · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
26
09
value_loss: first 0.002153 → final 0.00002170; min 0.00001931, max 0.002153; 196 logged samples.
Notes: Metric matrix: numerical audit of this trace · 3/3 value_loss: first 0.002153 → final 0.00002170; min 0.00001931, max 0.002153; 196 logged samples. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 27
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Verification: define success before looking · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
27
01
A smoke profile is only a four-transition pipeline check and is not skill evidence.
02
Require deterministic evaluation to report every complete requested episode; reject incomplete, nonfinite, assisted-after-release, unsupported, or failed seeds.
03
Check the 600-step three-stage gate separately from the 600-step landing-only gate.
04
Confirm assist_after_release_steps is zero before crediting PPO landing behavior.
Notes: Verification: define success before looking · 1/3 A smoke profile is only a four-transition pipeline check and is not skill evidence. Require deterministic evaluation to report every complete requested episode; reject incomplete, nonfinite, assisted-after-release, unsupported, or failed seeds. Check the 600-step three-stage gate separately from the 600-step landing-only gate. Confirm assist_after_release_steps is zero before crediting PPO landing behavior. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 28
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Verification: define success before looking · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
28
05
Confirm handoff rotation is at least 5.8 rad and the pre-handoff PPO stability streak reaches 10 samples.
06
Confirm the final 100 landing-only samples meet the physical stability thresholds; a low gyro alone is insufficient.
07
Compare final and initializer raw landing returns seed by seed and repeat under fixed action noise before claiming PPO refinement.
08
Inspect rollout MP4 and contact sheet for airborne rotation, landing contact, controller stage labels, and final stand hold.
Notes: Verification: define success before looking · 2/3 Confirm handoff rotation is at least 5.8 rad and the pre-handoff PPO stability streak reaches 10 samples. Confirm the final 100 landing-only samples meet the physical stability thresholds; a low gyro alone is insufficient. Compare final and initializer raw landing returns seed by seed and repeat under fixed action noise before claiming PPO refinement. Inspect rollout MP4 and contact sheet for airborne rotation, landing contact, controller stage labels, and final stand hold. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 29
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Verification: define success before looking · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
29
09
Verify ONNX 61-to-14 contract and PyTorch/ONNX action parity, plus policy and stand-policy hash provenance.
Notes: Verification: define success before looking · 3/3 Verify ONNX 61-to-14 contract and PyTorch/ONNX action parity, plus policy and stand-policy hash provenance. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 30
SAVED RESULTS — NOT A NEW TRAINING RUN / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Results: what was actually measured · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
30
01
fact: The retained V5 default three-stage evaluation passed 16 of 16 complete 600-step showcase episodes. | source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json
02
fact: The independent audit passed 8 of 8 showcase episodes on seeds 801-808. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md
03
fact: With stand handoff removed, the final PPO actor passed 7 of 8 landing-only episodes; seed 808 did not hold all final 100 samples. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md
04
fact: Paired landing-only mean raw return regressed from 3409.02 for the initializer to 2978.57 for the final actor, a delta of -430.449 or -12.63 percent; 0 of 8 seeds improved. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md
Notes: Results: what was actually measured · 1/3 fact: The retained V5 default three-stage evaluation passed 16 of 16 complete 600-step showcase episodes. | source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json fact: The independent audit passed 8 of 8 showcase episodes on seeds 801-808. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md fact: With stand handoff removed, the final PPO actor passed 7 of 8 landing-only episodes; seed 808 did not hold all final 100 samples. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md fact: Paired landing-only mean raw return regressed from 3409.02 for the initializer to 2978.57 for the final actor, a delta of -430.449 or -12.63 percent; 0 of 8 seeds improved. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 31
SAVED RESULTS — NOT A NEW TRAINING RUN / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Results: what was actually measured · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
31
05
fact: Zero actions passed 0 of 8 landing-only episodes despite a near-zero final gyro; mean final height was about 0.0316 m and upright projection about 0.1351. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md
06
fact: Final and initialization ONNX parity maximum absolute action error was 9.53674e-07, and the 61-input/14-output contract passed. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md
07
fact: The first PPO update recorded mean_loss 0.0011691017134580761, policy_loss -0.0009841816499829292, value_loss 0.002153283334337175, approximate_kl 0.04449799966823775, and clip_fraction 0.282470703125. | source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl
Notes: Results: what was actually measured · 2/3 fact: Zero actions passed 0 of 8 landing-only episodes despite a near-zero final gyro; mean final height was about 0.0316 m and upright projection about 0.1351. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md fact: Final and initialization ONNX parity maximum absolute action error was 9.53674e-07, and the 61-input/14-output contract passed. | source: rlx/artifacts/backflip-e2e-20260908-v5/report.md fact: The first PPO update recorded mean_loss 0.0011691017134580761, policy_loss -0.0009841816499829292, value_loss 0.002153283334337175, approximate_kl 0.04449799966823775, and clip_fraction 0.282470703125. | source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 32
SAVED RESULTS — NOT A NEW TRAINING RUN / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Results: what was actually measured · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
32
09
fact: The final PPO update at env_steps 401408 recorded mean_loss -0.0035966151881439146, policy_loss -0.003618316142819822, value_loss 0.000021701008108720998, approximate_kl 0.004050072617246769, clip_fraction 0.049560546875, and explained_variance 0.9215395247283621. | source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl
10
fact: The assisted showcase passed its physical gate but the extended audit verdict is FAIL because PPO refinement and all-seed standalone landing success were false. | source: rlx/artifacts/backflip-e2e-20260908-v5/audit.json
Notes: Results: what was actually measured · 3/3 fact: The final PPO update at env_steps 401408 recorded mean_loss -0.0035966151881439146, policy_loss -0.003618316142819822, value_loss 0.000021701008108720998, approximate_kl 0.004050072617246769, clip_fraction 0.049560546875, and explained_variance 0.9215395247283621. | source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl fact: The assisted showcase passed its physical gate but the extended audit verdict is FAIL because PPO refinement and all-seed standalone landing success were false. | source: rlx/artifacts/backflip-e2e-20260908-v5/audit.json Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 33
EMBEDDED OFFLINE VIDEO / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Watch the actual saved rollout
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
33
BEFORE PLAY
Predict one success signal and one failure signal.
AFTER PLAY
Which claims does this clip support? What remains untested?
12.0 s saved MP4 • Click in PowerPoint Slide Show • Backup: videos/backflip-rollout.mp4
Notes: Saved policy video Source: rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/ep0.mp4 Embedded video bytes are copied unchanged, not regenerated and not sped up. A single video is not a seed sweep. PowerPoint playback requires a user click; use the included MP4 in a local player if a presentation viewer cannot decode embedded media. This is not an unassisted learned backflip. The simulator spotter supplies substantial launch energy and rotation. The final stand is not owned by PPO; alpha_stand.onnx takes over only after the PPO landing gate. Exact teacher transfer means the landing ability was not learned from scratch. V5 physical showcase success does not establish PPO improvement; paired landing-only return regressed and one independent landing seed failed. The reward can score an upright airborne pose; touchdown and support are enforced by a separate physical gate. Randomization, noise, delay, and random yaw were disabled in the retained run. The exported backflip.onnx is only the landing-stage actor, not a complete controller and not hardware deployment authorization. No result establishes real-robot safety, actuator feasibility, or sim-to-real robustness. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 34
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Limits and failure analysis · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
34
01
This is not an unassisted learned backflip. The simulator spotter supplies substantial launch energy and rotation.
02
The final stand is not owned by PPO; alpha_stand.onnx takes over only after the PPO landing gate.
03
Exact teacher transfer means the landing ability was not learned from scratch.
04
V5 physical showcase success does not establish PPO improvement; paired landing-only return regressed and one independent landing seed failed.
Notes: Limits and failure analysis · 1/2 This is not an unassisted learned backflip. The simulator spotter supplies substantial launch energy and rotation. The final stand is not owned by PPO; alpha_stand.onnx takes over only after the PPO landing gate. Exact teacher transfer means the landing ability was not learned from scratch. V5 physical showcase success does not establish PPO improvement; paired landing-only return regressed and one independent landing seed failed. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 35
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Limits and failure analysis · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
35
05
The reward can score an upright airborne pose; touchdown and support are enforced by a separate physical gate.
06
Randomization, noise, delay, and random yaw were disabled in the retained run.
07
The exported backflip.onnx is only the landing-stage actor, not a complete controller and not hardware deployment authorization.
08
No result establishes real-robot safety, actuator feasibility, or sim-to-real robustness.
Notes: Limits and failure analysis · 2/2 The reward can score an upright airborne pose; touchdown and support are enforced by a separate physical gate. Randomization, noise, delay, and random yaw were disabled in the retained run. The exported backflip.onnx is only the landing-stage actor, not a complete controller and not hardware deployment authorization. No result establishes real-robot safety, actuator feasibility, or sim-to-real robustness. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 36
PROPOSED PRACTICE — NOT MEASURED RESULTS / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Student lab: change one variable, keep the gates · 1/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
36
01
Draw a three-column timeline and assign every launch, landing, and stand action to spotter, PPO actor, or pretrained stand policy.
02
Using the observation table, identify which reward inputs are actor-observable and which acceptance checks are privileged evaluator signals.
03
Compute the PPO batch size, number of optimizer steps per update, and number of complete updates in 401,408 transitions.
04
Recalculate the reward upper and lower bounds from the six term weights.
Notes: Student lab: change one variable, keep the gates · 1/3 Draw a three-column timeline and assign every launch, landing, and stand action to spotter, PPO actor, or pretrained stand policy. Using the observation table, identify which reward inputs are actor-observable and which acceptance checks are privileged evaluator signals. Compute the PPO batch size, number of optimizer steps per update, and number of complete updates in 401,408 transitions. Recalculate the reward upper and lower bounds from the six term weights. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 37
PROPOSED PRACTICE — NOT MEASURED RESULTS / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Student lab: change one variable, keep the gates · 2/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
37
05
Compare the first and last update fields, then explain why smaller losses or KL do not prove a better landing.
06
Use the audit table to calculate the paired percentage change for one seed and compare it with the aggregate -12.63 percent result.
07
Inspect ep0.mp4 and list the visual evidence that distinguishes launch assistance, PPO landing, and stand handoff.
08
Design a fixed-noise paired evaluation that keeps the physical gate unchanged and tests whether a successor improves the initializer.
Notes: Student lab: change one variable, keep the gates · 2/3 Compare the first and last update fields, then explain why smaller losses or KL do not prove a better landing. Use the audit table to calculate the paired percentage change for one seed and compare it with the aggregate -12.63 percent result. Inspect ep0.mp4 and list the visual evidence that distinguishes launch assistance, PPO landing, and stand handoff. Design a fixed-noise paired evaluation that keeps the physical gate unchanged and tests whether a successor improves the initializer. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 38
PROPOSED PRACTICE — NOT MEASURED RESULTS / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Student lab: change one variable, keep the gates · 3/3
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
38
09
Write a one-sentence claim that is supported by the evidence and a second sentence that would overclaim.
Notes: Student lab: change one variable, keep the gates · 3/3 Write a one-sentence claim that is supported by the evidence and a second sentence that would overclaim. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 39
PPO ROBOTICS LAB / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Submit an experiment, not just a video
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
39
01
Before training: write one hypothesis, the changed parameter, the fixed baseline, seed list, acceptance criteria and time/transition budget.
02
During training: save the exact command, environment versions, initialization, checkpoint and raw reward/loss/KL metrics. Never overwrite the saved reference run.
03
After training: evaluate the frozen exported policy on matched seeds; include all failures, aggregate metrics, the full rollout video and a source-bound result table.
04
Rubric / 10: reproducibility 2; environment and reward explanation 2; PPO and metrics interpretation 2; honest verification 2; one evidence-based next experiment 2.
Notes: Submit an experiment, not just a video Before training: write one hypothesis, the changed parameter, the fixed baseline, seed list, acceptance criteria and time/transition budget. During training: save the exact command, environment versions, initialization, checkpoint and raw reward/loss/KL metrics. Never overwrite the saved reference run. After training: evaluate the frozen exported policy on matched seeds; include all failures, aggregate metrics, the full rollout video and a source-bound result table. Rubric / 10: reproducibility 2; environment and reward explanation 2; PPO and metrics interpretation 2; honest verification 2; one evidence-based next experiment 2. Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 40
REPOSITORY-RELATIVE PATHS / FULL SOURCES IN NOTES / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Source map and further study · 1/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
40
01
microduck_local/AGENTS.md
02
docs/student-book/microduck-lab-student-book.md
03
docs/backflip-showcase/REPORT.md
04
docs/backflip-showcase/recipe.json
Notes: Source map and further study · 1/2 microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.

## Slide 41
REPOSITORY-RELATIVE PATHS / FULL SOURCES IN NOTES / BACKFLIP: ASSISTED LAUNCH, PPO LANDING, AND STAND HANDOFF
Source map and further study · 2/2
MICRODUCK / SIMULATION EVIDENCE / 11 SEP 2026
41
05
docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md
06
docs/microduck-training-student-book/chapters/02b-gae-workshop.md
07
scripts/scenarios/README.md
08
README.md
Notes: Source map and further study · 2/2 docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Teaching protocol: ask students to predict the outcome before showing the evidence. Separate saved measurements, explanatory arithmetic, and proposed experiments. Never imply that these slides report newly trained policies or hardware validation. Case sources (repository-relative): microduck_local/AGENTS.md docs/student-book/microduck-lab-student-book.md docs/backflip-showcase/REPORT.md docs/backflip-showcase/recipe.json docs/backflip-showcase/lifecycle.svg rlx/rlx/environments/backflip.py rlx/rlx/environments/backflip_evaluation.py rlx/rlx/models/backflip_bootstrap.py rlx/examples/ppo_microduck_studio.py rlx/rlx/algorithms/ppo.py scripts/train-backflip.sh rlx/runs/studio/backflip/backflip-e2e-20260908-v5/backflip.safetensors.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/evaluation.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/render/evidence.json rlx/runs/studio/backflip/backflip-e2e-20260908-v5/training-metrics.jsonl rlx/artifacts/backflip-e2e-20260908-v5/audit.json rlx/artifacts/backflip-e2e-20260908-v5/report.md rlx/artifacts/backflip-e2e-20260908-v5/provenance.json PPO teaching references: docs/microduck-training-student-book/chapters/02a-ppo-code-lab.md docs/microduck-training-student-book/chapters/02b-gae-workshop.md scripts/scenarios/README.md README.md Evidence edition: 2026-09-11. Complete raw recorded metrics are bundled under raw/backflip/. For exact copyable commands and detailed case evidence, use the companion instructor guide and evidence/cases.json.